## Slide 1: Accessible Route/ Path of Travel Under DOT ADA Regulations November 7, 2013 John Day ADA Team Leader

## Slide 2: What is a Path of Travel?
A continuous, unobstructed way of pedestrian passage by means of which an area may be approached, entered, and exited
  Related term: Accessible Route

## Slide 3: Why Is This Important?
ADA compliance
  Condition of eligibility for Federal funding
  FTA is responsible for ensuring ADA compliance on the part of its grantees
Risk reduction
  Reduced potential for delayed grants
  Reduced exposure to litigation/enforcement action
  Cheaper to do it right the first time!

## Slide 4: Why Is This Important?
Recurring issue among FTA projects
  New Construction
  Alterations to existing stations/facilities
State of Good Repair
  Projects will likely contain activities regarded as “alterations” under DOT ADA regulations

## Slide 5: What is the ADA?
Common misconceptions:
  “It means you have to make reasonable accommodations for people with disabilities.”
  “It’s all about paratransit.”
  “It means you have to figure out how to get wheelchairs onto your bus/into your station.”

## Slide 6: What is the ADA?
A comprehensive civil rights law that ensures that people with disabilities have the same rights and responsibilities as everyone else.

## Slide 7: General Requirements for Facilities
All new construction must be accessible
Any alterations to any existing facility must be accessible
Standards are the same, but application may be different
Path-of-travel/accessible route is addressed in requirements for both

## Slide 8: General Requirements for Facilities
“Accessible” means complying with DOT ADA standards.
  Don’t try to figure it out on your own!
Use the right standard!
  DOT ADA standards for buildings & facilities updated November 29, 2006
    Different from Access Board’s 2004 standards
    Different from DOJ’s “2010 Standards”

## Slide 9: General Requirements for Facilities
ADA MYTHBUSTERS
Myth: “We’re using our own funds, so we don’t have to worry about ADA regulations.”
Facts: ADA requirements – and DOT ADA regulations – apply regardless of Federal funding
  Compliance is a condition of eligibility for Federal funding
  No FTA funding means no FTA oversight – but compliance is still required

## Slide 10: General Requirements for Facilities
ADA MYTHBUSTERS
Myth: “We’re using our own funds, so we don’t have to worry about ADA regulations.”
Facts: ADA requirements – and DOT ADA regulations – apply regardless of Federal funding
  Compliance is a condition of eligibility for Federal funding
  No FTA funding means no FTA oversight – but compliance is still required

## Slide 11: New Construction
Differences in DOT Standards
  Minimize accessible route/path of travel
  Detectable warnings at curb ramps
Different from 1991 Standards
  60% of entrances must be accessible
    Formerly 50%
    One of two entrances is not 60%

## Slide 12: New Construction
Minimize accessible route/path of travel
  “Elements such as ramps, elevators, or other circulation devices, fare vending or other ticketing areas, and fare collection areas shall be placed to minimize the distance which wheelchair users and other persons who cannot negotiate steps may have to travel compared to the general public.” [DOT Standards, Section 206.3]
May affect how station is designed
May require elevators in lieu of ramps

## Slide 13: New Construction
Path of travel not minimized:

## Slide 14: New Construction
Path of travel not minimized:

## Slide 15: New Construction
Reaction to South Attleboro (MA) Station (c. 1989)

## Slide 16: New Construction
Reaction to South Attleboro (MA) Station (c. 1989)

## Slide 17: New Construction
Ramps and Stairs Coexisting Peacefully
Notes: This slide added in response to questions concerning “break points” for ramps vs. elevators
There is none; the distance of the accessible route must be minimized with respect to the distance others must travel
This example is from a theme park, and is illustrative only; cannot confirm compliance re: slope, landings, etc.

## Slide 18: New Construction
Detectable warnings at curb ramps
Required under DOT ADA regulations
  Continuation of original ADAAG requirement
Not included in DOJ “2010 Standards”
Not included in Access Board’s 2004 revisions

## Slide 19: New Construction
Other important elements for rail facilities:
  Flangeway gap must not exceed 2.5”
    If cannot be achieved, overpass/underpass may be required
    Overpass/underpass may require elevators

## Slide 20: New Construction
Other important elements for transportation facilities:
  Accessible routes must coincide with or be located in the same area as general circulation paths.
  Where circulation paths are interior, accessible routes must also be interior.
  Walks, unpaved paths and vehicular ways designed for pedestrian traffic must be accessible or have an accessible route nearby.
  Elevators must be in the same area as stairs and escalators, not isolated in the back of the facility.

## Slide 21: New Construction Do’s & Don'ts
If you are contemplating construction of a facility or part of a facility…
Do:
  Use the right standards
  Specify the right standards in contracts!
  Plan and budget to ensure that the facility or part of the facility constructed will comply with ADA standards upon completion
Don’t:
  Don’t rely solely on standards issued by county, municipality, state
  Don’t rely on building inspectors, certificates of occupancy or other local “approvals”
  Don’t rely on simple references to incorporate ADA requirements (e.g., “All facilities shall be ADA compliant.”)
  Don’t attempt to “avoid” certain ADA requirements

## Slide 22: Alterations to Existing Facilities
ADA MYTHBUSTERS
Myth: “It’s not a key station, so it doesn’t have to be accessible”
Facts: “Key stations” represented a deadline
  Certain stations would have to be made accessible by a date-certain
  Regardless of short- or long-term plans
  To ensure a basic level of system accessibility within a reasonable timeframe

## Slide 23: Alterations to Existing Facilities
ADA MYTHBUSTERS
Myth: “It’s not a key station, so it doesn’t have to be accessible”
Facts: “Key stations” represented a deadline
  Certain stations would have to be made accessible by a date-certain
  Regardless of short- or long-term plans
  To ensure a basic level of system accessibility within a reasonable timeframe

## Slide 24: Alterations to Existing Facilities
What is an alteration?
  A change to an existing facility, including, but not limited to:
    Remodeling
    Renovation
    Rehabilitation
    Reconstruction
    Historic restoration
    Changes or rearrangement in structural parts or elements
    Changes or rearrangement in the plan configuration of walls and full-height partitions
  (49 CFR 37.3)

## Slide 25: Alterations to Existing Facilities
What is not an alteration?
  Normal maintenance activities, unless they affect the usability of the building or facility
    Reroofing
    Painting or wallpapering
    Asbestos removal
    Changes to mechanical or electrical systems
(49 CFR 37.3)

## Slide 26: Alterations to Existing Facilities
What standards apply to alterations?
  Same standards as for new construction
  Application of those standards may be different
    “To the maximum extent feasible” – The occasional case where the nature of the facility makes it impossible to fully comply [49 CFR 37.43(b)]
    In some cases, slightly steeper ramp slopes are permitted.
    Other examples: door thresholds, curb ramp landings, handrails, etc.

## Slide 27: Alterations to Existing Facilities
When an alteration affects an area containing a “primary function,” an additional requirement is triggered to make the path of travel to the altered area accessible, unless the cost and scope would be “disproportionate” [49 CFR 37.43(a)(2)]
  A “primary function” is a major activity for which the facility is intended [49 CFR 37.43(c)]
    Ticket purchase and collection areas
    Passenger waiting areas
    Train or bus platforms
  “Disproportionate” is defined as exceeding 20% of the cost of the alteration to the area of primary function, without regard to the costs of accessibility modifications [49 CFR 37.43(e) ]

## Slide 28: Alterations to Existing Facilities
ADA MYTHBUSTERS
Myth: “Federal law requires that at least 20% of the cost of the alterations must be spent on making the altered facility accessible.”
Facts:
  Alterations must be accessible
  20% “disproportionality” only applies to additional alterations to the path of travel that are triggered when a primary function area is altered

## Slide 29: Alterations to Existing Facilities
ADA MYTHBUSTERS
Myth: “Federal law requires that at least 20% of the cost of the alterations must be spent on making the altered facility accessible.”
Facts:
  Alterations must be accessible
  20% “disproportionality” only applies to additional alterations to the path of travel that are triggered when a primary function area is altered

## Slide 30: Alterations to Existing Facilities
Example: Disproportionality
Sunnydale Station (Hill Valley Transit/HVT)
  Platform resurfacing
    Resurfacing = alteration (per ADA-ABA AG 106.5)
    Platform = primary function
    Alteration to platform triggers path of travel requirement
  HVT documented that the cost of installing elevators to each platform would exceed 20% of the resurfacing cost.

## Slide 31: Alterations to Existing Facilities
HVT Sunnydale Station

## Slide 32: Alterations to Existing Facilities
Example: “Maximum Extent Feasible”
Tremorton Transit (TTA) Red Line
  Complete platform replacement at 7 elevated stations
    Platform = primary function
    Removal/replacement = alteration
    Path of travel requirement triggered
  TTA demonstrated insufficient clearances on narrow platforms to accommodate elevators (without exponential increase in cost/scope of alterations)

## Slide 33: Alterations to Existing Facilities
TTA Danville Station

## Slide 34: Alterations to Existing Facilities
When the altered area is the path of travel, the path of travel has to be accessible
  Altered areas must be accessible
  Disproportionality does not apply
  Infeasibility may apply

## Slide 35: Alterations to Existing Facilities
Example: Altered Area Is Path of Travel
Metroville Transit Authority (MTA)
  Substantial rehabilitation at several stations
    Platform, station house & staircases
    All areas containing primary functions
    Alteration to staircase = alteration to path of travel
  MTA provided information for each station demonstrating specific site conditions that made elevators not feasible
    Removal of travel lanes from streets under stations
    Significantly reduced overhead clearance above streets beneath stations
Determined on basis of infeasibility (site-specific conditions); disproportionality not a factor

## Slide 36: Alterations to Existing Facilities
MTA Traction Avenue

## Slide 37: Alterations to Existing Facilities
Jurisdictional Issues
  City owns facility
  Transit system operates service
All entities involved must work together
  All may not be FTA grantees
  Grantee will have to demonstrate attempt to bring parties together
  Can’t parse responsibilities when facilities are connected

## Slide 38: Alterations to Existing Facilities
Example: Jurisdictional Issues
Lassiter Plaza (Metroville)
  Bus transfer facility owned by City of Metroville, served by MTA, connected to OmniTrain commuter rail station below
  City of Metroville undertaking alterations to bus transfer facility and surrounding pedestrian infrastructure
  Existing stairwell connecting OmniTrain station directly to Plaza would be come primary entrance
  Existing accessible entrance to OmniTrain station some distance away

## Slide 39: Alterations to Existing Facilities
Lassiter Plaza (Metroville)

## Slide 40: Alteration Do’s & Don'ts
If you are contemplating alterations to a facility or part of a facility…
Do:
  Use the right standards
  Plan and budget to ensure that the altered areas will comply with ADA standards upon completion
  Know whether the altered areas contain a primary function
    If not, know why not
    If so, plan and budget for additional alterations to the path of travel

## Slide 41: Alteration Do’s & Don'ts
Do:
  Show your work!
    Document any site-specific conditions that make it infeasible to meet specific requirements
    Demonstrate coordination with any other affected entities
    Provide documented support for any claims that alterations to the path of travel would be disproportionate
    FTA should be able to independently reach the same conclusions upon review of documentation
    A picture is worth a thousand words; plans and architectural drawings are worth considerably more

## Slide 42: Alteration Do’s & Don'ts
Don’t:
  Don’t describe major renovations with terms like “maintenance” or “repairs”
  Don‘t describe maintenance or repair activities with terms like “renovation” or “rehabilitation”
  Don’t plan to “avoid” requirements

## Slide 43: Alteration Do’s & Don'ts
Remember:
Infeasibility and disproportionality are not “waivers”
  Does not require “FTA approval”
  However, grants require FTA approval, and ADA compliance is a condition of all FTA grants
  Absence of adequate documentation can delay grant approval
Any altered features that can be made accessible must be made accessible. [49 CFR 37.43(b) ]
alteration

## Slide 44: Alteration Do’s & Don'ts
Remember:
There is no such thing as “replacement in kind”
  Not contemplated in DOT ADA regulations
  Cannot simply replace an element or feature with an identical element or feature
There is no such thing as “partial compliance”
  Full compliance is required
  What constitutes full compliance can vary according to specific circumstances

## Slide 45
Federal Transit Administration
www.fta.dot.gov